| List of Bulletins for M137AZ engine - service | 1a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M137AZ/1 |  |  | Cancelled |  |  |
| M137AZ/2 | M137A/7 | 16.8.1976 | Corrections of oil pressure specification at idle run of the M137 and M137AZ engines and of maximum permissible temperature of cylinder heads (metered under the ignition plugs in the engine R.H. side. | M |  |
| M137AZ/3 | M137A/8 M337/73 M337A/2 | 28.3.1977 | Split-pin-locking of connecting rod bold castellated nuts of the new M137A, M137AZ, M337 and M337A engines and these engines of following Serial Numbers. | M |  |
| M137AZ/4 |  |  | Cancelled |  |  |
| M137AZ/5a |  |  | Cancelled |  |  |
| M137AZ/6a | M137A/11a M337A/5a M337AK/2a | 24.5.1985 | The inprovement of the deareation of the LUN 5150.01 fuel injection pump mounted on M137A, M137AZ, M337A and M337AK engines. | M |  |
| M137AZ/7a | M137A/12a M337A/6a M337AK/3a | 16.7.1985 | Modification of the venting ball valve in the cover of the injection pump fuel chamber LUN 5150.01. | M |  |
| M137AZ/8a | M137A/13a | 30.9.1992 | The V 503A propeller flange D/N Sh 4017, engine M137A/AZ, aircraft Z 42 and Z 50M. | M |  |
| M137AZ/9a | M332/67a M332A/1a M137A/14a M337/75a M337A/8a M337AK/5a | 7.9.1994 | How time (calendar months) effect time between overhauls (TBO) for the following reciprocating engines M332, M332A, M137, M137AZ, M337, M337A and M337AK. | M |  |
| M137AZ/10a | M332/70a M332A/2a M332AK/1a M137A/15a M337/81a M337A/9a M337AK/6a M337AK.1/1a M132A/1a M132AK/1a | 6.6.1996 | Application of cylinder head Sc 2706 marked „Z“ together with special plain washers – cylinder head stud bolt nut Sc 1504R for all types and versions of engines stated above. | M |  |

| List of Bulletins for M137AZ engine - service | 2a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M137AZ/11a |  |  | Cancelled |  |  |
| M137AZ/12a | M332/75a M332A/9a M332AK/8a M137A/17a M337/85a M337A/11a M337AK/8a M132A/6a M132AK/6a | 7.1.1998 | Precision of fuel mixture enrichement by engine starting, by engine operation in different flight levels and by landing. | M |  |
| M137AZ/13a/R1 | M332/76a/R1 M332A/10a/R1 M332AK/9a/R1 M332B/5a M332C/1a M137A/18a/R1 M137AZ/13a/R1 M137C/1a M337A/12a/R1 M337AK/9a/R1 M337B/5a M337C/1a M132A/7a/R1 M132AK/7a/R1 M132C/1a | 3.12.2003 | Upgraded list of necessary documentation for checking, repairing, service and O/Hs. | M |  |

| List of Bulletins for M137AZ engine - service | 3a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M137AZ/14a | M332/78a M332A/11a M332AK/10a M137A/19a M337/89a M337A/13a M337AK/10a M337AK.1/9a M132A/8a M132AK/8a M332B/1a M337B/1a | 18.12.1998 | Tightening moment for the tightening screws of oil pumps S/N : Sh 0059, Sh 0060, Sh 0060AK, Sc 0060 and Sh 0060A,B,C,D (for M337B, M332B engines). | M |  |
| M137AZ/15a | M332/82a M332A/15a M332AK/14a M132A/12a M132AK/12a M137A/20a M337/93a M337A/14a M337AK/11a | 23.10.2000 | The time restriction for idling operation during engine test on the ground for aircraft engines M337, M332, M137, M132 of all series. | M |  |
| M137Az/16a | M132A/13a M132AK/13a M332A/16a M332AK/15a M137A/21a M337A/15a M337AK/12a | 5.4.2001 | Technical description and Operator´s Manual for operation of engines M337A/AK, M332A/AK, M137A/AZ, M132A,AK (hereinnafter Operator´s Manual. | M |  |
| M137AZ/17a |  |  | Cancelled |  |  |

| List of Bulletins for M137AZ engine - service | 4a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M137AZ/18a | M332/85a M332A/18a M332AK/17a M132A/14a M132AK/14a M137A/23a M337/96a M337A/17a M337AK/14a M337AK.1/15a | 22.10.2001 Valid from 1.1.2002 | Supplementary verification of airworthiness and issuance of authorized release certificate by an authorized person (form: JAA FORM ONE) for new or already used and repaired spare parts, assemblies, subassemblies and units (hereafter as: spare parts) for engines M337, M137, M332, M132 - all versions, for which no admissible documents confirming airworthiness have been issued, or which are doubtful. | M |  |

Revision date:  August 31, 2018