| List of Bulletins for M337A engine - service | 1a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/1 |  |  | Cancelled |  |  |
| M337A/2 | M137A/8 M137AZ/3 M337/73 | 28.3.1977 | Split-pin-locking of connecting rod bold castellated nuts of the new M137A, M137AZ, M337 and M337A engines and these engines of following Serial Numbers. | M |  |
| M337A/3 |  |  | Cancelled |  |  |
| M337A/4a |  |  | Cancelled |  |  |
| M337A/5a | M137A/11a M137AZ/6a M337AK/2a | 24.5.1985 | The inprovement of the deareation of the LUN 5150.01 fuel injection pump mounted on M137A, M137AZ, M337A and M337AK engines. | M |  |
| M337A/6a | M137A/12a M137AZ/7a M337AK/3a | 16.7.1985 | Modification of the venting ball valve in the cover of the injection pump fuel chamber LUN 5150.01. | M |  |
| M337A/7a |  |  | Cancelled |  |  |
| M337A/8a | M332/67a M332A/1a M137A/14a M137AZ/9a M337/75a M337AK/5a | 7.9.1994 | How time (calendar months) effect time between overhauls (TBO) for the following reciprocating engines M332, M332A, M137, M137AZ, M337, M337A and M337AK. | M |  |
| M337A/9a | M332/70a M332A/2a M332AK/1a M137A/15a M137AZ/10a M337/81a M337AK/6a M337AK.1/1a M132A/1a M132AK/1a | 6.6.1996 | Application of cylinder head Sc 2706 marked „Z“ together with special plain washers – cylinder head stud bolt nut Sc 1504R for all types and versions of engines stated above. | M |  |

| List of Bulletins for M337A engine - service | 2a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/10a |  |  | Cancelled |  |  |
| M337A/11a | M332/75a M332A/9a M332AK/8a M137A/17a M137AZ/12a M337/85a M337AK/8a M132A/6a M132AK/6a | 7.1.1998 | Precision of fuel mixture enrichement by engine starting, by engine operation in different flight levels and by landing. | M |  |
| M337A/12a/R1 | M332/76a/R1 M332A/10a/R1 M332AK/9a/R1 M332B/5a M332C/1a M137A/18a/R1 M137AZ/13a/R1 M137C/1a M337A/12a/R1 M337AK/9a/R1 M337B/5a M337C/1a M132A/7a/R1 M132AK/7a/R1 M132C/1a | 3.12.2003 | Upgraded list of necessary documentation for checking, repairing, service and O/Hs. | M |  |

| List of Bulletins for M337A engine - service | 3a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/13a | M332/78a M332A/11a M332AK/10a M137A/19a M137AZ/14a M337/89a M337AK/10a M337AK.1/9a M132A/8a M132AK/8a M332B/1a M337B/1a | 18.12.1998 | Tightening moment for the tightening screws of oil pumps S/N : Sh 0059, Sh 0060, Sh 0060AK, Sc 0060 and Sh 0060A,B,C,D (for M337B, M332B engines). | M |  |
| M337A/14a | M332/82a M332A/15a M332AK/14a M132A/12a M132AK/12a M137A/20a M137AZ/15a M337/93a M337AK/11a | 23.10.2000 | The time restriction for idling operation during engine test on the ground for aircraft engines M337, M332, M137, M132 of all series. | M |  |
| M337A/15a | M132A/13a M132AK/13a M332A/16a M332AK/15a M137A/21a M137AZ/16a M337AK/12a | 5.4.2001 | Technical description and Operator´s Manual for operation of engines M337A/AK, M332A/AK, M137A/AZ, M132A,AK (hereinnafter Operator´s Manual. | M |  |
| M337A/16a |  |  | Cancelled |  |  |

| List of Bulletins for M337A engine - service | 4a |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/17a | M332/85a M332A/18a M332AK/17a M132A/14a M132AK/14a M137A/23a M137AZ/18a M337/96a M337AK.1/15a | 22.10.2001 Valid from 1.1.2002 | Supplementary verification of airworthiness and issuance of authorized release certificate by an authorized person (form: JAA FORM ONE) for new or already used and repaired spare parts, assemblies, subassemblies and units (hereafter as: spare parts) for engines M337, M137, M332, M132 - all versions, for which no admissible documents confirming airworthiness have been issued, or which are doubtful. | M |  |

Revision date  August 31, 2018