| List of Bulletins for M337AK.1 engine | 1 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337AK.1/1a | M332/70a M332A/2a M332AK/1a M137A/15a M137AZ/10a M337/81a M337A/9a M337AK/6a M132A/1a M132AK/1a | 6.6.1996 | Application of cylinder head Sc 2706 marked „Z“ together with special plain washers – cylinder head stud bolt nut Sc 1504R for all types and versions of engines stated above. | M |  |
| M337AK.1/2b |  |  | Cancelled |  |  |
| M337AK.1/3a |  | 17.3.1997 | Issue of a new independent „Technical description and maintenance manual for M337AK.1 engine“. | M |  |
| M337AK.1/4b | M 332A/5b M 332AK/4b M137A/21b M137AZ/14b M 337A/16b M337AK/11b M132A/2b M132AK/2b | 21.7.1997 | Introduction of modernised injection pump with automatic fuel mixture enrichement correction. |  | M |
| M337AK.1/5b | M332/72b M332A/7b M332AK/6b M137A/22b M137AZ/15b M337/83b M337A/17b M337AK/12b M132A/4b M132AK/5b | 6.10.1997 | Improvement of ignition magnetos sealing against oil leakage from engine crank case. |  | M |
| M337AK.1/6b |  |  | Not issued. |  |  |
| M337AK.1/7a |  | 22.6.1998 | M337AK.1 engines stored by Czech Army as reserve. | M |  |

| List of Bulletins for M337AK.1 engine | 2 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337AK.1/8b |  | Day of receiving | Possibility of T.B.O. increase for agregates after 1000 operating hrs. on M337AK.1 engines operated by Czech Army. |  | M |
| M337AK.1/9a | M332/78a M332A/11a M332AK/1a M137A/19a M137AZ/14a M337/89a M337A/13a M337AK/1a M132A/8a M132AK/8a M332B/1a M337B/1a | 18.12.1998 | Tightening moment for the tightening screws of oil pumps S/N : Sh 0059, Sh 0060, Sh 0060AK, Sc 0060 and Sh 0060A,B,C,D (for M337B, M332B engines). | M |  |
| M337AK.1/10a |  |  | Not issued. |  |  |
| M337AK.1/11b | M332/80b M332A/13b M332AK/12b M137A/26b M137AZ/19b M337/91b M337A/21b M337AK/16b M132A/10b M132AK/10b M332B/3bM337B/3b |  | Cancelled. |  |  |
| M337AK.1/12a |  | 18.10.1999 | Revokation of checking after 50 operation hrs. and its exchange for checking after 10010 operation hrs. on M337AK.1 engines operated by Czech Army. Changes in M337AK.1 engine operator´s manual for Czech Army. | M |  |

| List of Bulletins for M337AK.1 engine | 3 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337AK.1/13b |  | 19.10.1999 | Recommendation of oil pump exchange from Sh 0060AK to Sh 0602 in case of M337AK.1 engines operated by Czech Army. |  | M |
| M337AK.1/14a | M332/82a M332A/15a M332AK/14a M132A/12a M132AK/12a M137A/20a M137AZ/15a M337/93a M337A/14a M337AK/11a | 23.10.2000 | The time restriction for idling operation during engine test on the ground for aircraft engines M337, M332, M137, M132 of all series. | M |  |
| M337AK.1/15a | M332/85a M332A/18a M332AK/17a M132A/14a M132AK/14a M137A/23a M137AZ/18a M337/96a M337A/17a M337AK/14a | 22.10.2001 Valid from 1.1.2002 | Supplementary verification of airworthiness and issuance of authorized release certificate by an authorized person (form: JAA FORM ONE) for new or already used and repaired spare parts, assemblies, subassemblies and units (hereafter as: spare parts) for engines M337, M137, M332, M132 - all versions, for which no admissible documents confirming airworthiness have been issued, or which are doubtful. | M |  |
| M337AK.1/16b | M332/86b M332A/19b M332AK/18b M132A/15b M132AK/15b M137A/28b M137AZ/21b M337/97b M337A/23b M337AK/18b | 15.11.2001 | Change of top limit cylinder head temperature for normal operating range to value 195o C ( 383 o F ). |  | M |

| List of Bulletins for M337AK.1 engine | 4 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337AK.1/17b | M332/87b M332A/20b M332AK/19b M332B/4b M132A/16b M132AK/16b M137A/29b M137AZ/22b M337/98b M337A/24b M337AK/19b M337B/4b M337C/1b | 7.11.2001 Valid from 1.1.2002 | Possible use of BA91N, BA95N, BA98N vehicle gasolinesin accordance with CSN EN 228 in operation of M132, M332, M137 a M337 all version engines. |  | M |
| M337AK.1/18b |  |  | Not issued |  |  |
| M337AK.1/19b | M337A/25b M337AK/20b | 16.6.2003 | Iddle motor oil pressure and motor rpm in operation of Z43 and Z142 all version planes powered by M337A, M337AK, M337AK.1 engines. |  | M |
| M337AK.1/20b | M332/88b M332A/21b M332AK/20b M332B/6b M332C/2b M132A/17b M132AK/17b M132C/2b M137A/30b M137AZ/23b M137C/2b M337/99b M337A/26b M337AK/21b M337B/6b M337C/3b | 29.3.2005 | Possible use of minerál oil Exxon Mobil Aviation Oil EE100 for continuous flight operation of the M337, M332, M137, M132 engines in all versions. |  | M |

Revision date :   August 31, 2018